## Slide 1: cBR-8 Three-Step Dynamic Modulation TOI
John Downey
April 2016

## Slide 2: Agenda
Background
Feature Description
Sample Config
Show Commands
Debugging and Test Commands

## Slide 3: Background
Spectrum management provides facility to automatically select modulation profile of US ch based on RF statistics
  Advanced spectrum management uses spectrum groups and allows freq hopping & ch width changes
Dynamic modulation supported on cBR-8 whether spectrum group assigned to US ch or fixed frequency
Following RF statistics continue to be used in same manner as basic Dynamic Modulation found on uBR10K
  Ranging MER (dB)
  Correctable FEC (%)
  Uncorrectable FEC (%)
CNiR measurements not used for modulation change because ingress noise cancellation makes CNiR unreliable
  CNiR used for freq hopping & ch width changes
Note: Threshold values set to 0 are bypassed

## Slide 4: Feature Downgrade Algorithm
Downgrade from high performance mod profile to mid-level when following is true:
  (SNR ≤ (SNR Threshold 1)) AND
  [(cFEC ≥ (cFEC Threshold)) OR (uFEC ≥ (uFEC Threshold))]
Downgrade from high performance mod profile or mid-level to most robust profile when following is true:
  (SNR ≤ (SNR Threshold 2)) AND
  [(cFEC ≥ (cFEC Threshold)) OR (uFEC ≥ (uFEC Threshold))]
Note: May be best to set Corr FEC threshold to 0 to bypass
Note: First “hop” is instantaneous, but secondary upgrade or downgrade waits on 15 sec hold-down timer, which is not configurable

## Slide 5: Feature Upgrade Algorithm
Upgrade from most robust profile to mid-level when following is true:
  (SNR ≥ ((SNR Threshold 2) + Hysteresis)) AND
  (cFEC ≤ (cFEC Threshold)) AND
  (uFEC ≤ (uFEC Threshold))
Upgrade from mid-level profile to high profile when following is true:
  (SNR ≥ ((SNR Threshold 1) + Hysteresis)) AND
  (cFEC ≤ (cFEC Threshold)) AND
  (uFEC ≤ (uFEC Threshold))
    Hysteresis default value is 3 dB
Note: Upgrade will not go directly from lowest to highest; it must go to mid first, then wait for 15 sec timer & re-evaluate

## Slide 6: Basic US Modulation Profile
cBR-8 requires global modulation, so DOCSIS mode is in profile config
  cab modu 225 atdma request 0 16 0 22 16qam scram 152 no-diff 32 fixed qpsk1 1 2048
  cab modu 225 atdma initial 5 34 0 48 16qam scram 152 no-diff 384 fixed qpsk1 1 2048
  cab modu 225 atdma station 5 34 0 48 16qam scram 152 no-diff 384 fixed qpsk1 1 2048
  cab modu 225 atdma a-short 6 76 7 22 64qam scram 152 no-diff 64 short qpsk1 1 2048
  cab modu 225 atdma a-long 9 232 0 22 64qam scram 152 no-diff 64 short qpsk1 1 2048
Preamble for IM & SM bursts should be 384 and will update automatically when pre-eq activated
US chip may not allow other than QPSK or 16-QAM for first 3 bursts
Use 16-QAM SM burst whenever modulation >= 16-QAM for data traffic
  Flaplist (D3.0 Modem Diagnostics Log; “MDL”)
  Ping DOCSIS
  Possible effect on levels and modulation error ratio (MER)
    Note: Using QPSK with QPSK1 vs QPSK0 preamble may negate this
  PRE-EQ
  US channel bonding partial mode
    New Data Burst MER Threshold feature precedes/compliments this
SM sent every 15-20 sec, but T4 multiplier based on US bonding affects it

## Slide 7: More Modulation Profile Options
Initial Maintenance (IM) burst option
  cab modu 225 atdma init 5 34 0 48 qpsk scram 152 no-diff 384 fix qpsk0 1 2048
  A-short burst option for more roburst cm status messages
    cab modu 225 atdma a-sh 6 76 7 22 16qam scram 152 no-diff 64 sh qpsk1 1 2048
Can activate US dynamic interleave on a-long burst
  cab modu 225 atdma a-lo 9 232 0 22 64qam scram 152 no-diff 64 sh qpsk1 0 2048
  Could also activate on a-short burst, but effect is questionable
Another option is to use 16-QAM on a-UGS burst for VoIP and 236 B CW size to cover 4B VLAN if needed
  cab modu 225 atdma a-ugs 9 236 0 22 16qam scram 152 no-diff 64 sh qpsk1 1 2048
Option for a-UGS VoIP burst when using IPV6
  cab modu 225 atdma a-ugs 7 128 0 22 64qam scram 152 no-diff 64 sh qpsk1 1 2048
Special suggested profile for RFoG systems
  cab modu 224 reques 0 16 0 70 qpsk scram 152 no-diff 36 fixed qpsk0 1 2048
  cab modu 224 initia 5 34 0 48 qpsk scram 152 no-diff 384 fixed qpsk0 1 2048
  cab modu 224 statio 5 34 0 48 16qam scram 152 no-diff 384 fixed qpsk1 1 2048
  cab modu 224 a-shor 6 76 6 40 64qam scram 152 no-diff 64 short qpsk1 1 2048
  cab modu 224 a-long 9 232 0 40 64qam scram 152 no-diff 64 short qpsk1 1 2048
  cab modu 224 a-ugs 9 232 0 40 64qam scram 152 no-diff 64 short qpsk1 1 2048
Notes: Change IM burst to QPSK to allow more robust registration and longer time on the wire for the inti(r1) burst to help alleviate possible collisions or susceptibility to noise. I would keep the Request burst at 16-QAM because it can affect the amount of scheduled time (minislots) when doing nRTPS or RTPS for call signaling or multicast. Same if doing UGS-AD since it goes to nRTPS when a call is on mute.

## Slide 8: Configure Modulation Profiles
Configure three different modulation profiles; most robust, mid-level, and high-performance
cab modu 222 request 0 16 0 22 qpsk scram 152 no-diff 32 fixed qpsk0 1 2048
cab modu 222 initial 5 34 0 48 qpsk scram 152 no-diff 384 fixed qpsk0 1 2048
cab modu 222 station 5 34 0 48 qpsk scram 152 no-diff 384 fixed qpsk0 1 2048
cab modu 222 a-short 4 76 7 22 qpsk scram 152 no-diff 64 short qpsk0 1 2048
cab modu 222 a-long 9 232 0 22 qpsk scram 152 no-diff 64 short qpsk0 1 2048
cab modu 222 a-ugs 9 232 0 22 qpsk scram 152 no-diff 64 short qpsk0 1 2048
cab modu 223 request 0 16 0 22 16qam scram 152 no-diff 32 fixed qpsk1 1 2048
cab modu 223 initial 5 34 0 48 16qam scram 152 no-diff 384 fixed qpsk1 1 2048
cab modu 223 station 5 34 0 48 16qam scram 152 no-diff 384 fixed qpsk1 1 2048
cab modu 223 a-short 4 76 7 22 16qam scram 152 no-diff 64 short qpsk1 1 2048
cab modu 223 a-long 9 232 0 22 16qam scram 152 no-diff 64 short qpsk1 1 2048
cab modu 223 a-ugs 9 232 0 22 16qam scram 152 no-diff 64 short qpsk1 1 204
cab modu 224 request 0 16 0 22 16qam scram 152 no-diff 32 fixed qpsk1 1 2048
cab modu 224 initial 5 34 0 48 16qam scram 152 no-diff 384 fixed qpsk1 1 2048
cab modu 224 station 5 34 0 48 16qam scram 152 no-diff 384 fixed qpsk1 1 2048
cab modu 224 a-short 6 76 6 22 64qam scram 152 no-diff 64 short qpsk1 1 2048
cab modu 224 a-long 9 232 0 22 64qam scram 152 no-diff 64 short qpsk1 1 2048
cab modu 224 a-ugs 9 232 0 22 64qam scram 152 no-diff 64 short qpsk1 1 2048

## Slide 9: Sample Controller & Cable Interface Configs
cBR8(config)#controller Upstream-Cable 2/0/0
  us-channel 0 frequency 24000000
  us-channel 0 channel-width 6400000 6400000
  us-channel 0 threshold snr-profiles 24 19
  us-channel 0 threshold corr-fec 0
  us-channel 0 threshold hysteresis 4
  us-channel 0 docsis-mode atdma
  us-channel 0 minislot-size 2
  us-channel 0 modulation-profile 224 223 222
  us-channel 0 equalization-coefficient
  no us-channel 0 shutdown
cBR8(config)#interface Cable2/0/0
  load-interval 30
  downstream Integrated-Cable 2/0/0 rf-channel 0-7
  upstream 0 Upstream-Cable 2/0/0 us-channel 0
  cable upstream 0 power-adjust continue 6

## Slide 10: Obsolete Hopping Commands?
cBR8(config)#cab spectrum-group 1 ?
  band Band frequency setting
  hop Frequency hop configuration
  time Time setting
  Suggest to make multiple, 6.4 MHz wide bands
cBR8(config)#cab spectrum-group 1 hop ?
  period Minimum frequency hop period
  threshold Missing poll threshold which triggers frequency hop
  I think this command was before advance spectrum management and not used anymore
cBR8(config-controller)#us-channel 0 hop-priority ?
  frequency Frequency Priority
  modulation Modulation Priority
  Missing ch width and I think hop priority not set anymore

## Slide 11: Spectrum Groups with Freq & Ch Width Changes
cBR8#sh run | beg spectrum
  cable spectrum-group 1 band 16000000 22500000
  cable spectrum-group 1 band 22600000 29100000
  Note: It may be advantageous to make bands slightly bigger than 6.4 and/or separated slightly
cBR8(config)#controller Upstream-Cable 1/0/0
  us-channel 0 spectrum-group 1
  us-channel 0 channel-width 6400000 3200000
  us-channel 0 threshold snr-profiles 24 19
  us-channel 0 docsis-mode atdma
  us-channel 0 minislot-size 2
  us-channel 0 modulation-profile 224 223 222
  us-channel 0 equalization-coefficient
Note: Minislot changes automatically with ch width and we need to see what happens here

## Slide 12: Show Cable Modulation Commands
cBR8#sh cab modu 224
Mod Mode IUC Type Pre Diff FEC FEC Scrmb Max Grd Last Scrmb Pre Pre RS
len enco T k seed B time CW off Type
BYTE BYTE size short
224 atdma req 16qam 32 no 0x0 0x10 0x152 0 22 no yes 0 qpsk1 no
224 atdma ini 16qam 384 no 0x5 0x22 0x152 0 48 no yes 0 qpsk1 no
224 atdma sta 16qam 384 no 0x5 0x22 0x152 0 48 no yes 0 qpsk1 no
224 atdma a-s 64qam 64 no 0x6 0x4C 0x152 6 22 yes yes 0 qpsk1 no
224 atdma a-l 64qam 64 no 0x9 0xE8 0x152 0 22 yes yes 0 qpsk1 no
224 atdma a-u 64qam 64 no 0x9 0xE8 0x152 0 22 yes yes 0 qpsk1 no
cBR8#sh cab modulation-profile upstream-Cab 2/0/0 us-ch 0
Mod Mode IUC Type Pre Dif FEC FEC Scrmb Max Grd Last Scrmb Pre Pre RS
len enc T k seed B time CW off Type
BYTE BYTE siz siz short
224 atdma req 16qam 32 no 0x0 0x10 0x152 0 22 no yes 0 qpsk1 no
224 atdma ini 16qam 384 no 0x5 0x22 0x152 0 48 no yes 0 qpsk1 no
224 atdma sta 16qam 384 no 0x5 0x22 0x152 0 48 no yes 0 qpsk1 no
224 atdma a-s 64qam 64 no 0x6 0x4C 0x152 6 22 yes yes 0 qpsk1 no
224 atdma a-l 64qam 64 no 0x9 0xE8 0x152 0 22 yes yes 0 qpsk1 no
224 atdma a-u 64qam 64 no 0x9 0xE8 0x152 0 22 yes yes 0 qpsk1 no
  Note: This is more accurate and will show auto-updated parameters

## Slide 13: Verify Settings and Current Modulation
cBR#show run | sec spectrum-g (with limited band, simple case)
  cBR#cable spectrum-group 1 band 10000000 16400000
Check current modulation profile
  cBR8#sh contr c2/0/0 up 0 | in Modu
    Modulation Profile Group 224
    Modu (64-QAM) - A-short 64-QAM, A-long 64-QAM, A-ugs 64-QAM

## Slide 14: Show Cable Hop Commands
cBR8#sh cab hop upstream-cable 2/0/0 us-channel 0
Upstream Channel Poll Miss Min Miss Hop Hop Corr Uncorr
Channel Status Rate Poll Poll Poll Thres Period FEC FEC
(ms) Count Sample Pcnt Pcnt (sec) Errors Errors
UC2/0/0:U0 24.000 MHz 425 *** set to fixed frequency*** 6 7
cBR#show cable hop upstream-cable 2/0/0 us-channel 0 history
F = Frequency Hop, M = Modulation Change, C = Channel Width Change
Upstream Action Chg Chg Chg Action
Channel Time Code From To Reason
UC2/0/0:U0 Nov 10 11:54:41 M 222 223 SNR 33>=33
Nov 10 11:54:11 F 23.200 21.600 SNR 27<30
(add noise by 26 M) Nov 10 11:54:11 C 6.4 3.2 SNR 27<30
Nov 10 11:53:40 M 223 222 SNR 27<30
Nov 10 11:48:01 M 224 223 SNR 33<35
Nov 10 11:44:56 F 0.000 23.200 Config changed
Nov 10 11:44:50 C 1.6 6.4 Config changed
cBR#show cable hop upstream-cable 2/0/0 us-channel 0 threshold
Upstream SNR(dB) CNR(dB) CorrFEC% UncorrFEC% MissedSM%
Channel Val Thre1 Thre2 Val Thre1 Thre2 Pcnt Thre Pcnt Thre Pcnt Thre
UC2/0/0:U0 33 35 30 33 30 25 0 0 0 0 0 50

## Slide 15: Show Controller Commands
cBR#show controllers upstream-Cable 2/0/0 us-channel 0
USPHY OFDMA support: NO
Controller 2/0/0 upstream 0 AdminState:UP OpState: UP
atdma mode enabled
Frequency 21.600 MHz, Channel Width 6.400 MHz, Symbol Rate 5.120 Msps
Modulation Profile Group 223
Modulations (16-QAM) - A-short 16-QAM, A-long 16-QAM, A-ugs 16-QAM
Mapped to connector 0 and receiver 12
Bind to Cable2/0/0 US0
US phy MER(SNR)_estimate for good packets - 33.100 dB
Spectrum Group 2
CNR measurement : 33 dB
Nominal Input Power Level 0 dBmV
part_id=0x3142, rev_id=0xC0, rev2_id=0x00
Range Load Reg Size=0x2C
Request Load Reg Size=0x07
Minislot Size in number of Timebase Ticks is = 2
Minislot Size in Symbols = 32
Minislot Size in Bytes = 16

## Slide 16: Debugging Commands
cBR#debug cable specmgmt
cBR#debug cable specmgmt upstream-cable x/y/z us-ch n
cBR#debug cable specmgmtfreqhop
cBR#debug cable specsvl qband